## Slide 1
Face poking on crystal skull
2025-08-13 | t = 0 at peak_pre_idx (onset candidate) | window 0.4–1.2 s vs -2–0 s
Take-home: cortex is time-locked to the poke; a region map still needs spatial footprints.

## Slide 2
Experiment
Whole dorsal cortex Ca2+ imaging while a motor arm pokes the face. Every movie on this day is a poking session — there is no no-poke baseline.

## Slide 3
Two recordings of the same experiment
s00 = 8.38 mW/cm2, s01 = 20 mW/cm2. mirror1 and mirror2 are two optical paths (two FOVs at the same time).

## Slide 4
How poke time is defined
No behavior camera. A blocker on the arm changes mean-frame intensity. t = 0 is peak_pre_idx: the intensity minimum just before the positive brightness peak (candidate stimulus onset).

## Slide 5
How traces are analyzed
EXTRACT traces at 33 Hz. Cut -2 to +3 s around each poke. A cell is excited or inhibited if 0.4–1.2 s differs from -2–0 s (Wilcoxon signed-rank, p<0.05).

## Slide 6
What we cannot show yet
Fig4 is a session-average picture of the FOV. To paint which cortical regions are excited vs inhibited, Omer needs to export spatial_weights as a normal sparse matrix.

## Slide 7
All recordings together
12 movies | same alignment and windows

## Slide 8
Fig1 Population PSTH | all movies
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: Activity dips at poke onset, then rises and peaks about 1.5 s later — a delayed, poke-locked population response.

## Slide 9
Fig2 Neuron STA | all movies
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: A subset of cells go up after the poke and another subset go down; the all-cell mean is small because they partly cancel.

## Slide 10
Fig3 Excited vs inhibited cells | all movies
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: About 5–13% of cells are excited and 17–24% inhibited; only 5 of 12 movies pass the population test with this window.

## Slide 11
Fig4 FOV anatomy (not a response map) | all movies
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: Cells are dense across dorsal cortex, but this picture cannot say which regions turned on or off after poking.

## Slide 12
Fig5 Trial raster and poke interval | all movies
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: About 48–57 pokes per movie; median interval is 5.3 s (set to 3 s, with mechanical jitter). Long gaps are missed peaks.

## Slide 13
Fig1 Population PSTH | mouse1f s00 8.38 mW/cm2 mirror1
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 1240 neurons and 56 pokes; the population pre vs post test is significant (p = 0.021).

## Slide 14
Fig2 Neuron STA | mouse1f s00 8.38 mW/cm2 mirror1
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 9.0% and inhibited 21.3% of 1240 neurons; see the STA split on the right.

## Slide 15
Fig3 Excited vs inhibited cells | mouse1f s00 8.38 mW/cm2 mirror1
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 9.0% excited, 21.3% inhibited out of 1240 neurons; population test significant (p = 0.021).

## Slide 16
Fig4 FOV anatomy (not a response map) | mouse1f s00 8.38 mW/cm2 mirror1
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 17
Fig5 Trial raster and poke interval | mouse1f s00 8.38 mW/cm2 mirror1
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 56 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 18
Fig1 Population PSTH | mouse1f s00 8.38 mW/cm2 mirror2
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 1930 neurons and 55 pokes; the population pre vs post test is not significant (p = 0.143).

## Slide 19
Fig2 Neuron STA | mouse1f s00 8.38 mW/cm2 mirror2
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 9.4% and inhibited 21.1% of 1930 neurons; see the STA split on the right.

## Slide 20
Fig3 Excited vs inhibited cells | mouse1f s00 8.38 mW/cm2 mirror2
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 9.4% excited, 21.1% inhibited out of 1930 neurons; population test not significant (p = 0.143).

## Slide 21
Fig4 FOV anatomy (not a response map) | mouse1f s00 8.38 mW/cm2 mirror2
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 22
Fig5 Trial raster and poke interval | mouse1f s00 8.38 mW/cm2 mirror2
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 55 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 23
Fig1 Population PSTH | mouse1f s01 20 mW/cm2 mirror1
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 2786 neurons and 57 pokes; the population pre vs post test is significant (p = 2.4e-04).

## Slide 24
Fig2 Neuron STA | mouse1f s01 20 mW/cm2 mirror1
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 12.0% and inhibited 17.2% of 2786 neurons; see the STA split on the right.

## Slide 25
Fig3 Excited vs inhibited cells | mouse1f s01 20 mW/cm2 mirror1
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 12.0% excited, 17.2% inhibited out of 2786 neurons; population test significant (p = 2.4e-04).

## Slide 26
Fig4 FOV anatomy (not a response map) | mouse1f s01 20 mW/cm2 mirror1
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 27
Fig5 Trial raster and poke interval | mouse1f s01 20 mW/cm2 mirror1
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 57 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 28
Fig1 Population PSTH | mouse1f s01 20 mW/cm2 mirror2
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 3749 neurons and 57 pokes; the population pre vs post test is significant (p = 3.8e-05).

## Slide 29
Fig2 Neuron STA | mouse1f s01 20 mW/cm2 mirror2
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 13.0% and inhibited 17.8% of 3749 neurons; see the STA split on the right.

## Slide 30
Fig3 Excited vs inhibited cells | mouse1f s01 20 mW/cm2 mirror2
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 13.0% excited, 17.8% inhibited out of 3749 neurons; population test significant (p = 3.8e-05).

## Slide 31
Fig4 FOV anatomy (not a response map) | mouse1f s01 20 mW/cm2 mirror2
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 32
Fig5 Trial raster and poke interval | mouse1f s01 20 mW/cm2 mirror2
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 57 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 33
Fig1 Population PSTH | mouse2c s00 8.38 mW/cm2 mirror1
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 2097 neurons and 57 pokes; the population pre vs post test is not significant (p = 0.125).

## Slide 34
Fig2 Neuron STA | mouse2c s00 8.38 mW/cm2 mirror1
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 7.9% and inhibited 19.8% of 2097 neurons; see the STA split on the right.

## Slide 35
Fig3 Excited vs inhibited cells | mouse2c s00 8.38 mW/cm2 mirror1
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 7.9% excited, 19.8% inhibited out of 2097 neurons; population test not significant (p = 0.125).

## Slide 36
Fig4 FOV anatomy (not a response map) | mouse2c s00 8.38 mW/cm2 mirror1
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 37
Fig5 Trial raster and poke interval | mouse2c s00 8.38 mW/cm2 mirror1
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 57 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 38
Fig1 Population PSTH | mouse2c s00 8.38 mW/cm2 mirror2
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 2889 neurons and 57 pokes; the population pre vs post test is significant (p = 0.021).

## Slide 39
Fig2 Neuron STA | mouse2c s00 8.38 mW/cm2 mirror2
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 9.0% and inhibited 19.6% of 2889 neurons; see the STA split on the right.

## Slide 40
Fig3 Excited vs inhibited cells | mouse2c s00 8.38 mW/cm2 mirror2
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 9.0% excited, 19.6% inhibited out of 2889 neurons; population test significant (p = 0.021).

## Slide 41
Fig4 FOV anatomy (not a response map) | mouse2c s00 8.38 mW/cm2 mirror2
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 42
Fig5 Trial raster and poke interval | mouse2c s00 8.38 mW/cm2 mirror2
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 57 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 43
Fig1 Population PSTH | mouse2c s01 20 mW/cm2 mirror1
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 3012 neurons and 56 pokes; the population pre vs post test is not significant (p = 0.419).

## Slide 44
Fig2 Neuron STA | mouse2c s01 20 mW/cm2 mirror1
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 6.1% and inhibited 21.1% of 3012 neurons; see the STA split on the right.

## Slide 45
Fig3 Excited vs inhibited cells | mouse2c s01 20 mW/cm2 mirror1
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 6.1% excited, 21.1% inhibited out of 3012 neurons; population test not significant (p = 0.419).

## Slide 46
Fig4 FOV anatomy (not a response map) | mouse2c s01 20 mW/cm2 mirror1
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 47
Fig5 Trial raster and poke interval | mouse2c s01 20 mW/cm2 mirror1
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 56 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 48
Fig1 Population PSTH | mouse2c s01 20 mW/cm2 mirror2
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 4022 neurons and 56 pokes; the population pre vs post test is not significant (p = 0.267).

## Slide 49
Fig2 Neuron STA | mouse2c s01 20 mW/cm2 mirror2
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 6.5% and inhibited 20.5% of 4022 neurons; see the STA split on the right.

## Slide 50
Fig3 Excited vs inhibited cells | mouse2c s01 20 mW/cm2 mirror2
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 6.5% excited, 20.5% inhibited out of 4022 neurons; population test not significant (p = 0.267).

## Slide 51
Fig4 FOV anatomy (not a response map) | mouse2c s01 20 mW/cm2 mirror2
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 52
Fig5 Trial raster and poke interval | mouse2c s01 20 mW/cm2 mirror2
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 56 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 53
Fig1 Population PSTH | mouse2c s02 power TBD mirror1
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 1407 neurons and 55 pokes; the population pre vs post test is not significant (p = 0.968).

## Slide 54
Fig2 Neuron STA | mouse2c s02 power TBD mirror1
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 5.5% and inhibited 23.9% of 1407 neurons; see the STA split on the right.

## Slide 55
Fig3 Excited vs inhibited cells | mouse2c s02 power TBD mirror1
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 5.5% excited, 23.9% inhibited out of 1407 neurons; population test not significant (p = 0.968).

## Slide 56
Fig4 FOV anatomy (not a response map) | mouse2c s02 power TBD mirror1
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 57
Fig5 Trial raster and poke interval | mouse2c s02 power TBD mirror1
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 55 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 58
Fig1 Population PSTH | mouse2c s02 power TBD mirror2
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 2040 neurons and 54 pokes; the population pre vs post test is not significant (p = 0.240).

## Slide 59
Fig2 Neuron STA | mouse2c s02 power TBD mirror2
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 5.9% and inhibited 22.2% of 2040 neurons; see the STA split on the right.

## Slide 60
Fig3 Excited vs inhibited cells | mouse2c s02 power TBD mirror2
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 5.9% excited, 22.2% inhibited out of 2040 neurons; population test not significant (p = 0.240).

## Slide 61
Fig4 FOV anatomy (not a response map) | mouse2c s02 power TBD mirror2
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 62
Fig5 Trial raster and poke interval | mouse2c s02 power TBD mirror2
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 54 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 63
Fig1 Population PSTH | m3 (LabVIEW m1f) s00 mirror1
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 1537 neurons and 55 pokes; the population pre vs post test is significant (p = 0.018).

## Slide 64
Fig2 Neuron STA | m3 (LabVIEW m1f) s00 mirror1
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 9.8% and inhibited 22.9% of 1537 neurons; see the STA split on the right.

## Slide 65
Fig3 Excited vs inhibited cells | m3 (LabVIEW m1f) s00 mirror1
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 9.8% excited, 22.9% inhibited out of 1537 neurons; population test significant (p = 0.018).

## Slide 66
Fig4 FOV anatomy (not a response map) | m3 (LabVIEW m1f) s00 mirror1
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 67
Fig5 Trial raster and poke interval | m3 (LabVIEW m1f) s00 mirror1
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 55 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 68
Fig1 Population PSTH | m3 (LabVIEW m1f) s00 mirror2
What: Mean population activity (z-score) and fraction of active cells, aligned to each poke (t = 0 is peak_pre_idx).
Result: This FOV has 2148 neurons and 48 pokes; the population pre vs post test is not significant (p = 0.831).

## Slide 69
Fig2 Neuron STA | m3 (LabVIEW m1f) s00 mirror2
What: Each neuron’s average trace around the poke, sorted by response size; right panel is the mean of excited vs inhibited cells.
Result: Excited 6.7% and inhibited 21.8% of 2148 neurons; see the STA split on the right.

## Slide 70
Fig3 Excited vs inhibited cells | m3 (LabVIEW m1f) s00 mirror2
What: Per neuron: mean z in 0.4–1.2 s after t=0 vs -2–0 s before; signed-rank, p<0.05, sign of the difference.
Result: 6.7% excited, 21.8% inhibited out of 2148 neurons; population test not significant (p = 0.831).

## Slide 71
Fig4 FOV anatomy (not a response map) | m3 (LabVIEW m1f) s00 mirror2
What: EXTRACT session-mean image: average brightness over the whole movie, not pre vs post poke.
Result: This is only where cells sit in this FOV — not which cells responded to the poke.

## Slide 72
Fig5 Trial raster and poke interval | m3 (LabVIEW m1f) s00 mirror2
What: One row per poke (population z over time) and the histogram of time between detected pokes.
Result: 48 pokes detected in this movie; intervals near 5.3 s, with occasional missed peaks.

## Slide 73
Next
Export spatial footprints → map excited vs inhibited cells onto cortex. Optionally also show the peak_idx alignment, which locks more tightly because the 0.4–1.2 s window was chosen for that peak.